## Slide 1: BLE mouse controlled by head movements
MBDE - Project
Stefan Schönbauer
st16m027

## Slide 2: Introduction
BLE Mouse controlled by head-movements
IMU to detect head-movements
z
x
y

## Slide 3: Hardware – Metawear C
nRF51 – Nordic Semiconductors
  2.4 GHz transceiver
  ARM® Cortex™-M0 32 bit MCU
  256 kB flash program memory
  16 kB RAM
BMI160 – Bosch Sensortec
  3-Axis Accelerometer
  3-Axis Gyroscope
Proprietary Firmware onboard

## Slide 4: Hardware - nRF51 DK
nRF5x development kit
  Onboard JLINK interface
  Programming / debugging other nRFx chips via single wire debug interface

## Slide 5: Toolchain / SDK / Drivers
Eclipse with GNU Arm Embedded Toolchain
  GCC
  GDB
nrfjprog - Programming Tool
  Command line tool to load FW via SWD
SDK nRF5 12.3.0
  Examples with makefiles for GCC
  Provides HID mouse BLE profile
BMI160 Driver
  Gyroscope configuration (sample rate, measurement range)
  Interrupt configuration
  Auto calibration

## Slide 6: SPI – Serial Peripheral Interface
nRF51
BMI160
SCK: Serial Clock (output from master)
MOSI: Master Out Slave In (data output from master)
MISO: Master In Slave Out (data output from slave)
SS: Slave Select (active low, output from master)
Master
Slave

## Slide 7: Implementation
Start
BLE INIT
SPI INIT
BMI160 INIT
GPIOTE INIT
Read GYRO
Send Mouse Pos
DATA Ready?

## Slide 8: Issues
SPI connection between nRF51 and BMI160
Hardware connection for debug interface
Bias error of gyroscope  autocalibration
Auto-Click
  No motion interrupt works
  The packet is not send

## Slide 9: Outlook
Device Firmware Update
Power optimization
Fix mouse click issue
Better case